## Slide 1: Video-Based Road Damage Detection
Using Image Enhancement and Segmentation
Group 03 | 2nd Year Undergraduate | Department of Computing
Perera J A A D • Bandara M R V • Silva G B D • Gunarathna W A A I
Faculty of Applied Sciences | Rajarata University of Sri Lanka

## Slide 2: Problem Statement
2
Road Damage is Widespread
Sri Lankan roads face potholes, cracks, patch failures, and edge cracking due to
heavy traffic and adverse weather.
Manual Inspection is Inadequate
Current assessments are expensive, labour-intensive, time-consuming, and subjective — inconsistent results across inspectors.
Scale Challenge
Monitoring large national road networks manually is impractical and unsustainable.
Why It Matters
Vehicle Damage
Increased operating costs
Safety Risk
Accidents due to poor roads
Economic Loss
Maintenance budget inefficiency
Sri Lanka Focus
Mihintale, Anuradhapura, residential roads

## Slide 3: Project Objectives
3
01 Develop a Video-Based System
Design and implement an image processing pipeline that detects road surface damages from mobile video footage.
02 Apply Frame Enhancement
Use grayscale conversion, noise reduction, CLAHE contrast enhancement, illumination correction, and edge sharpening to improve frame quality.
03 Perform Reliable Segmentation
Apply Black-Hat morphological transform, binary thresholding, morphological closing, and connected component analysis to isolate damage regions.
04 Evaluate System Performance
Measure accuracy, precision, recall, F1-score, and IoU against ground truth; validate under varying environmental conditions.

## Slide 4: Video Acquisition Method
Recording Device
Apple iPhone 11
Resolution: 1920×1080 (Full HD) Frame Rate: 30 FPS
Duration: 15–30 sec per clip
Recording Sites
Mihintale • Kanadarawa • Anuradhapura New Town
Residential roads (tar & concrete)
Urban, semi-urban, and rural environments
Ethical Compliance: No identifiable individuals or licence plates captured. Recordings in public areas only.
Damage Types Captured
Surface Cracks
Patch Failures
Potholes Edge Cracking
Road Marking Removal
Frame Extraction Process
Every 10th frame extracted (uniform sampling – reduces redundancy)
Saved as JPEG • Original resolution preserved
Annotated with LabelImg (bounding box ground truth)

## Slide 5: Frame Enhancement Pipeline
5
1
Grayscale
RGB → single intensity channel Gray = 0.299R + 0.587G + 0.114B
2
Denoise
Median filter (salt & pepper) Gaussian filter (Gaussian noise)
3
CLAHE
Local contrast enhancement Clip limit: 2.0, Tile: 8×8
4
Illumination
Background normalization Corrected = Image / Background
5
Sharpen
Unsharp masking 2.0×Image − 1.0×Blur
Quantitative Improvement (Sample Frame)
Metric | Original Frame | Enhanced Frame | Improvement
Intensity Range | 120 | 198 | +65%
Laplacian Variance (Sharpness) | 85.3 | 162.7 | +91%
Mean Intensity | 92.4 | 110.6 | +20%

## Slide 6: Segmentation Pipeline
6
Enhanced Image | 
Gaussian Blur (5×5) | 
Black-Hat Transform (25×25) | 
Binary Threshold (value > 35) | 
Morphological Closing (5×5, ×2) | 
Area Filtering (0.08%–30%) | 
Final Segmented Output | 
Black-Hat Transform
Tblackhat = Closing(I) − I
Isolates dark regions SMALLER than a 25×25 kernel → targets cracks/potholes,
ignores large shadows.
Morphological Closing
Closing(A,B) = (A ⊕ B) ⊖ B
Bridges fragmented crack segments, ensuring structural continuity for accurate severity assessment.
Dynamic Area Filtering
Accepts contours between 0.08% and 30% of frame area.
Eliminates gravel noise (too small) and false shadow regions (too large).

## Slide 7: Integrated Processing Pipeline
Frame Extraction
Every 10th frame Saved as JPEG
Enhancement
Grayscale → Denoise CLAHE → Illumination
→ Sharpen
4-Stage End-to-End Video Processing
1 2 3
Segmentation
Median Blur → Adaptive Threshold → Morph Clean
→ Component Filter
4
Contour Marking
Draw red contours over enhanced frame
Frames
Original extracted frames
Enhanced
5-stage enhanced grayscale frames
Segmented
Binary damage mask images
Final_Output
Contour-marked final images
Key Pipeline Loop (integrated_code.py)
while True:
frame = cap.read() # extract enhanced = enhance_frame(frame) # enhance mask = get_segmentation_mask(...) # segment marked = draw_damage_contours(...) # mark & save
Pipeline Statistics
Frame Interval: Every 10th frame
Output Folders: 4 (Frames / Enhanced / Segmented / Final)
Format: JPEG · Original resolution preserved
Processing: Sequential per-frame pipeline

## Slide 8: Visual Comparison
Original Image Enhanced Image
Final Output
Segmented Image

## Slide 9: Cont...
Original Image
Enhanced Image
Final Output
Segmented Image

## Slide 10: Experimental Setup
7
Dataset Summary |  |  |  | 
Video | Damage Type | Frames Extracted | Frames Tested | Conditions
V1 | Crack | 100 | 30 | Mixed lighting
V2 | Pothole | 120 | 35 | Bright + shadow
V3 | Patch Failure | 90 | 25 | Uneven illumination
V4 | Edge Cracking | 70 | 30 | Shadow + low contrast
Total | 4 types | 380 | 120 | Real-world variation
Enhancement Parameters | 
Gaussian Kernel | 5×5
Median Window | 5×5
CLAHE Clip Limit | 2.0
CLAHE Tile Size | 8×8
Illumination Kernel | 71×71
Sharpen (α / β) | 2.0 / −1.0
Segmentation Parameters | 
Enhancement Blur | 5×5 Gaussian
Black-Hat Kernel | 25×25 rectangle
Binary Threshold | Pixel value > 35
Morphological Close | 5×5, 2 iterations
Min Area Filter | 0.08% of frame
Max Area Filter | 30% of frame

## Slide 11: Results & Evaluation
8
Segmentation Performance by Damage Type (120 test frames) |  |  |  |  | 
Damage Type | Accuracy | Precision | Recall | F1-Score | IoU
Crack | 0.92 | 0.90 | 0.84 | 0.89 | 0.78
Pothole | 0.95 | 0.94 | 0.90 | 0.93 | 0.85
Patch Failure | 0.90 | 0.88 | 0.81 | 0.86 | 0.75
Edge Cracking | 0.91 | 0.89 | 0.80 | 0.87 | 0.76
1
0.8
0.6
0.4
0.2
0
Crack
Edge Cracking
IoU & F1-Score by Damage Type
Pothole
IoU
Patch Failure
F1-Score
Key Findings
Potholes achieved highest IoU (0.85) – strong boundary detection
Black-Hat transform successfully eliminated shadow false positives
Dynamic area filter removed gravel noise while preserving thin cracks
Average accuracy >90% across all damage categories

## Slide 12: Limitations
9
Extreme Shadows
Very dark shadows cannot be fully removed by normalization — residual dark patches may be mistaken for cracks during segmentation.
Wet Road Conditions
Surface reflections from rain alter pixel intensity profiles, potentially causing false detections or missed damage regions.
Motion Blur
Excessive camera shake or fast movement blurs crack edges into road texture, reducing recall in blur-heavy frames.
Compression Artifacts
Block noise from MP4 video encoding can persist after filtering, introducing unwanted texture patterns.
Non-Structural Anomalies
Dark tire marks, oil spills, or wet patches mimic pothole intensity profiles, occasionally causing false positives.
Patch Boundary Over-segmentation
The algorithm sometimes segments patch boundaries as multiple individual cracks rather than a single unified region.

## Slide 13: Conclusion & Future Work
Conclusions
A complete video-based road damage detection system was successfully
designed and implemented using mobile footages from Sri Lankan roads.
The 5-stage enhancement pipeline consistently improved image quality —
intensity range +65%, sharpness +91%.
The Black-Hat segmentation approach eliminated shadow-based false positives that global thresholding (Otsu) could not handle.
Average segmentation accuracy exceeded 90% across four damage categories with potholes achieving IoU of 0.85.
The system provides a scalable, low-cost alternative to manual road inspection.
Future Work
Deep Learning Integration
Use CNN/YOLO-based models for real-time classification
Temporal Consistency
Frame-to-frame tracking to filter transient noise
Adaptive Parameters
Dynamic area thresholds based on camera perspective
Shape-Based Filtering
Eccentricity/circularity to distinguish cracks from oil spots
Advanced Enhancement
Deep learning-based denoising for extreme conditions
GitHub: github.com/BinadiSilva/road_damage_detection | Group 03 | ICT2403

## Slide 14: THANK YOU !